ANNEX A - Specifications

UNHCR UKRAINE Invitation to Bid ITB 2019-01

Construction materials for Assistance provided to Internally Displaced Persons (IDPs)

- QUANTITY OF PRODUCTS

Bidders should confirm ability to supply goods in the following quantities:

| # | Description, size in millimeters | Indicative annual quantity | Measure |
| --- | --- | --- | --- |
| 1 | Timber - battens (25x100x4500) | 30,000.00 | pcs |
|  | Timber - battens (25x150x4500) | 13,000.00 | pcs |
|  | Timber - planks (50x50x4500) | 2,500 | pcs |
|  | Timber - planks (100x100x4500) | 500 | pcs |
|  | Timber - planks (50x150x4500) | 5,000.00 | pcs |
|  | Timber - planks (70x150x4500) | 1,000 | pcs |
|  | Timber - planks (100x200x4500) | 5,048 | pcs |
|  | Timber – Lath (20 x 25 x 3000) | 20,000 | pcs |
| 2 | External doors, metal, with frame, 2100х900 mm | 60 | pcs |
| 3 | Brick (silicate), 25 x 12 x 8,8 cm | 20,100.00 | pcs |

- SPECIFICATION OF PRODUCTS

The products should comply with specification described below.

Timber

| Description | Material | Quality of drying / humidity % | Strength class / Standard | Sort | Antibacterial treatment | Deviation size, corresp. GOST 25346-89 | Compliance with radiological control/ certificate | The nominative content of CS-137 Bq/kg - no more | The activity of CS-137 Bq/kg - no more | Certificate of origin of wood | A phytosanitary certificate issued by the State Veterinary and Phytosanitary Service of Ukraine | Conclusion of the State sanitary-epidemiological expertise for applied antiseptic |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Timber - batterns (25x100x4500) | Pine or fir tree, density P<0.5 (g/cm3) | CAT III / no more than 12% | Class C27 according to MGB 52001 | Sort - 2 | yes | IT (13-17) | yes | 740 | 5 | yes | yes | yes |
| Timber - batterns (25x150x4500) |  |  |  |  |  |  |  |  |  |  |  |  |
| Timber - planks (50x50x4500) |  |  |  | Sort - 1 |  |  |  |  |  |  |  |  |
| Timber - planks (100x100x4500) |  |  |  |  |  |  |  |  |  |  |  |  |
| Timber - planks (50x150x4500) |  |  |  |  |  |  |  |  |  |  |  |  |
| Timber - planks (70x150x4500) |  |  |  |  |  |  |  |  |  |  |  |  |
| Timber - planks (100x200x4500) |  |  |  |  |  |  |  |  |  |  |  |  |
| Timber - Lath (20x25x3000) |  |  |  |  |  |  |  |  |  |  |  |  |

Required delivery timeframe for 30% of the forecasted annual quantity: No more than 20 calendar days.

External doors

| External door, metal, with frame, 2100х900 mm Standards: ISO БВ.2.6-11: 2011 |
| --- |
| Property | Quality |
| Size of door panel (without the door-box) | 2100х900 mm |
| Metal of the canvas | Cold steel - not less than 2 mm |
| Metal of the frame | Cold steel - not less than 2 mm |
| Box thickness | At least 139 mm |
| Canvas thickness | At least 98,5 mm |
| Ribs | 4 pcs |
| Frame filler | Mineral wool |
| Hinges | Metal with angular contact bearing |
| Q-ty of hinges | At least 2 |
| Anti-removal crossbars with hand loop | Available |
| Condensation | Three contours |
| Additional protective plates | Near the locks 1,2 mm thickness. |
| Cover | "Hammer”, alkyd-based |
| Group of breach protection | AV-1 |
| Warranty and lifetime | 1 year and 10 years |
| Accessories | Door knob and two Mortise locks (wing-key and cylinder) |
| Conformity | DSTU Б В.2.6-11:2011 |
| Certificates | UkrSEPRO , Conclusion of the state sanitary and epidemiological examination |
| Required delivery timeframe for 30% of the forecasted annual quantity | No more than 20 calendar days |

Brick

| Facing Silicate Thickened Brick with the brand of strength of 150 Standards: СПЛ – 150/1,6/25 DSTU B.V. (ДСТУ Б.В) 2.7-80:2008 |
| --- |
| Property | Quality |
| Size | 250мм*120мм*88мм |
| Material | Silicate |
| Color | White |
| Standard | Compliance with DSTU B V. (ДСТУ Б.В.) 2.7-80:2008 |
| Brand of strength | 150 |
| Class average density | 1.6 |
| Mark of frost resistance | F25 |
| Usage | For external walls |
| Certificates | Conformity |
| Required delivery timeframe for 30% of the forecasted annual quantity | No more than 20 calendar days |

C - PACKAGING, LABELLING FOR TRANSPORTATION

The bidder shall describe the proposed packaging for transportation and defining a packing unit (PU). The quantity of items in each PU must be standardized and this information must be clearly specified along with its weight, volume and the equipment required for handling it in the technical offer.

D- PRODUCTION AND DELIVERY CAPACITY

The bidder shall state its annual production capacity and the quantities available after 20 days of production lead-time.

The bidder shall state existing stock quantity available for immediate dispatch and the delivery time. In addition, the lead-time for delivery of the forecasted annual quantity of materials from date of receipt of Purchase Order must be specified (no more than 30 calendar days).

The Supplier may be requested to deliver products to Kurakhovo, Sievierodonetsk, Slavyansk, Mariupol, Kyiv. Time, conditions and limitations of such delivery shall also be stated.