ANNEX A - Specifications

UNHCR UKRAINE RFQ 2020-141,

on the supply of roofing materials, foam mounting, nails and roofing ridges

- PRODUCT SPECIFICATIONS

| Lot | Item | Specification | Quantity |
| --- | --- | --- | --- |
| 1 | Roofing Ridge | zinced steel, 200x200x2000mm, 0,4-0,5mm thickness, edge rolled inside | 1500 pcs |
| 2 | Roofing material | Basis: roofing cardboard. Roll size: 1x15m Area in a roll: 15 square meters. m Weight: 16.5 kg. | 1200 roll |
| 3 | Foam mounting | Application temperature: -5 ... + 30 ° C Volume: 750 ml Type of foam: professional Seasonality: all-season | 200 pcs |
| 4 | Nails roofing (shiffer) | Diameter: 5 mm Length: 120 mm Coating: without coating Material: steel Packed in bags/boxes 1 kilo each | 1500 kg |
|  | Nails 4*100mm | Material: steel Packed in bags/boxes 1 kilo each | 600 kg |
|  | Nails 3*70 mm | Material: steel Packed in bags/boxes 1 kilo each | 500 kg |

The compliance with the specification should be confirmed by a certificate of quality.