Annex A to RFQ 2021-102

PROVISION OF REPAIR AND MAINTENANCE SERVICES FOR UNHCR VEHICLES

Requirements:

- Scope of work and expected outcome:

Bids must confirm the possibility of providing the following services.

UNHCR has a requirement for maintenance and repair of:

- one (1) vehicles Volkswagen Caravelle Comfortline Long, 4Motion (4WD):

- DP 209 002 - Volkswagen Caravelle Comfortline Long, 4Motion (4WD) year of manufacture – 2019 / vehicle identification number – WV2ZZZ7HZKH114857

- estimative mileage per year – 20 000 km

General requirements:

- The Supplier must assign a manager to maintain UNHCR orders

- The Supplier must agree in writing (e-mail) on any additional works and costs with UNHCR and obtain the written consent of UNHCR prior to their implementation.

(I) Type of maintenances required:

1)      Intermediate maintenance - A type of maintenance (every 5 000 km)

  - check the level of oil, coolant, windshield wiper fluid

  - diagnostics of the general condition of the car: electricity, steering system, brake system, air conditioning system

  - oil change in the combustion engine

  - diagnostics of a running gear

  - greasing of a cardan shaft

  - replacement of the oil filter

  - replacement of cabin filter (if necessary)

  - replacement of the air filter (if necessary)

  - replacement of the fuel filter (if necessary)

  - wheel alignment

2)      Medium maintenance - B Type of maintenance (every 15 000 km)

  - check the level of oil, coolant, brake fluid, windshield wiper fluid

  - diagnostics of the general condition of the car: electricity, steering system, brake system, air conditioning system

  - check of oil level in a transmission (to top up if necessary)

  - oil change in the combustion engine

  - diagnostics of a running gear

  - greasing of a cardan shaft

  - replacement of the oil filter

  - replacement of the cabin filter

  - replacement of the air filter

  - replacement of the fuel filter

  - wheel alignment

3)    Full maintenance – C Type of maintenance (every 30 000 km)

  - check the level of oil, coolant, brake fluid, windshield wiper fluid

  - diagnostics of the general condition of the car: electricity, steering system, brake system, air conditioning system

  - check of oil level in a transmission (to top up if necessary)

  - oil change in the combustion engine

  - diagnostics of a running gear

  - greasing of a cardan shaft

  - replacement of the oil filter

  - replacement of the cabin filter

  - replacement of the air filter

  - replacement of the fuel filter

  - wheel alignment

  - oil change in the junction box

  - oil change in axles (front and rear)

  - replacement of brake fluid

4)    Every 60 000 km – D Type of maintenance.

  - check the level of oil, coolant, brake fluid, windshield wiper fluid

  - diagnostics of the general condition of the car: electricity, steering system, brake system, air conditioning system

  - check of a drive belt of hinged units and a set of rollers

  - oil change in the combustion engine

  - diagnostics of a running gear

  - greasing of a cardan shaft

  - replacement of the cabin filter

  - replacement of the oil filter

  - replacement of the air filter

  - replacement of the fuel filter

  - wheel alignment

  - oil change in the junction box

  - oil change in axles (front and rear)

  - replacement of radiator coolant

  - replacement of brake fluid

  - change of oil in a transmission

Pattern of required services for vehicles should be as per following:

A type of maintenance service – on 5,000 km;

A type of maintenance service – on 10,000 km;

B type of maintenance service – on 15,000 km;

A type of maintenance service – on 20,000 km;

A type of maintenance service – on 25,000 km;

C type of maintenance service – on 30,000 km;

A type of maintenance service – on 35,000 km;

A type of maintenance service – on 40,000 km;

B type of maintenance service – on 45,000 km;

A type of maintenance service – on 50,000 km;

A type of maintenance service – on 55,000 km;

D type of maintenance service – on 60,000 km;

A type of maintenance service – on 65,000 km;

A type of maintenance service – on 70,000 km;

B type of maintenance service – on 75,000 km;

A type of maintenance service – on 80,000 km;

A type of maintenance service – on 85,000 km;

C type of maintenance service – on 90,000 km;

A type of maintenance service – on 95,000 km;

Etc.

(II) Tire fitting “as and when required basis”;

Please provide the list of most common Tire fitting services with proposed prices (the range must be as full as possible);

(III) Body repair on “as and when required basis”;

Please provide the list of most common body repair services with proposed prices (the range must be as full as possible);

(IV) Engine and electrical repairs, including spare parts “as and when required basis”;

Please provide the list of most common spare parts, engine and electrical repairs and repairs with proposed prices (the range must be as full as possible);

Tentative list of works and spare parts

Diagnosis, cleaning and antibacterial treatment of the air conditioning system

Generator

Rear axle reducer

Front axle reducer

Shock-absorber rear

Thrust of the stabilizer of cross-section stability of a forward suspension bracket

Thrust of the stabilizer of lateral stability of a back-suspension bracket

Steering rack assembly

Power steering pump

Rear brake caliper

Front shock absorber support

Gearbox assembled

Body cushions, set

Windshield wiper

Check of fastening of a spare wheel

Casting wheels

Lighting equipment - check / fix / adjust

Checking electrical consumers and switches

Checking the condition of the battery

Cooling / heater system repair

Vacuuming and refueling of the air conditioning system

Checking the operation and lubrication of door locks

Replacement of a drive belt

Check the fuel tank, fuel line and valve

Steering wheel check (connection and backlash)

Inspection / repair of frame brackets

Check the condition of the body cushions

Diagnosis of a steering rack

Lubrication of guide calipers

Prevention of rear drum brakes

Handbrake - adjustment

Shock absorber front

Support of front shock-absorbing rack

Silentblocks of the front shock-absorber, kit

Lever upper left / right front axle

Lever lower left / right rear axle

Front suspension bumper

Rear shock absorber support

Front spring

Rear spring

Front stabilizer bushings

Rear stabilizer bushings

Traction bushings of the back stabilizer, kit

Thrust stabilizer front right

Thrust stabilizer front left

Thrust stabilizer rear right

Traction stabilizer rear left

Shock absorber rear left / right

Rear hub bearing right / left

Rear stabilizer bushings

Lever rear longitudinal upper

Lever rear longitudinal lower

Cardan shaft rear

Crosspiece of a cardan shaft

Cardan shaft front

Front brake disc

Rear brake disc

Handbrake pads (drum)

Handbrake cable, kit

Exhaust pipe (kit)

Cambelt

Front brake caliper

Rear brake caliper

Cost of norm-hour of work (add lines if they differ by type of work)

Welding works, UAH / standard hours

Hood painting

Roof painting

Painting of other elements (wing, bumper, door, …)

Installation - dismantling of a bumper

Installation - dismantling of a wing

Installation - dismantling of a headlight

Installation - disassembly of the hood

Gluing of outdoor logo

Cooling system repair

Fastening of a forward lattice of a radiator

Repair of wings

PTF repair

Intercooler purge

Cleaning the air conditioning system

Repair of plastic body components

Body straightening

Removal and installation of a forward reducer

Installation - dismantling of a loop of a cowl

Wheel repair

Computer diagnostics

Removal and installation of ICE protection

Electricity repair

Removing and installing the wheel

Tire fitting

Wheel balancing

Express sink

Complex car wash (interior, body)