ANNEX A – Specification to UKRKI/ RFQ / 2021-139

one-off procurement of electric carts for UNHCR projects in Ukraine

- SPECIFICATION

| # | Features | Requirements | Unit of measure | Q-ty |
| --- | --- | --- | --- | --- |
| 1. | Engine type | Electric | pcs | 2 |
|  | Engine capacity | Minimum 4 kW |  |  |
|  | Number of seats | 4 (3 passengers + 1 driver) |  |  |
|  | Maximum speed, km/hour | Minimum 25 km/hour |  |  |
|  | Maximum vertical lift gradient, % | Minimum 25 % |  |  |
|  | Radius of the U-turn | Maximum 4 meters |  |  |
|  | Mileage per full charge, km | Minimum 70 km |  |  |
|  | Power supply | 220/230 V |  |  |
|  | Temperature mode of operation | min -15˚C, max +30˚C |  |  |
|  | Clearance to the ground | Minimum 110 mm |  |  |
|  | Battery type | Maintenance-free battery |  |  |
|  | Year of production | no later than 2018 |  |  |
|  | Charger for charging through the electric grid |  |  |

- ADDITIONAL SPARE PARTS

- set of winter tires for each electric cart (two sets in total);

- set of conventional tires for each electric cart (two sets in total);

- two spare batteries of increased capacity for use during the cold season for each electric car (four batteries in total).

D- PACKAGING, LABELLING FOR TRANSPORTATION

The bidder shall describe the proposed packaging for transportation and defining a packing unit (PU). The quantity of items in each PU must be standardized and this information must be clearly specified along with its weight, volume and the equipment required to handle it in the technical offer. Each PU shall carry a label stating the content along with the Purchase Order number.

E- INDICATIVE IMAGE