Annex A to UKRKI/ RFQ/ 2022-161

FOR THE ESTABLISHMENT OF A FRAME AGREEMENT FOR MAINTENANCE, REPAIR, PROVISION OF SPARE PARTS AND CONSUMABLES FOR UNHCR FORD TRANSIT VEHICLES

Requirements:

- Scope of work and expected outcome:

Bids must confirm the possibility of providing the following services.

UNHCR has a requirement for maintenance and repair of:

- nine (9) vehicles FORD, TRANSIT MINIBUS, TRANSIT-350-L2-H2, Diesel, 2.0 TDCI, EURO 6, 9 Seats, MT, LHD

with the following VIN codes

WF0KXXTTRKNY27772

WF0KXXTTRKNY27776

WF0KXXTTRKNY27777

WF0KXXTTRKNY27778

WF0KXXTTRKNY27783

WF0KXXTTRKNY31087

WF0KXXTTRKNY31089

WF0KXXTTRKNY31091

WF0KXXTTRKNY34423

- year of production - 2021

- estimative mileage per year – 10 000 km

General requirements:

- The Supplier must assign a manager to maintain UNHCR orders

- The Supplier must agree in writing (e-mail) on any additional works and costs with UNHCR and obtain the written consent of UNHCR prior to their implementation.

- Cost of maintenance depending on the type:

Description

Type A maintenance – every 5 000 km: check the level of oil, coolant, windshield wiper fluid diagnostics of the general condition of the car: electricity, steering system, brake system, air conditioning system oil change in the combustion engine diagnostics of a running gear greasing of a cardan shaft replacement of the oil filter replacement of cabin filter (if necessary) replacement of the air filter (if necessary) replacement of the fuel filter (if necessary) wheel alignment

Type B maintenance – every 15 000 km: check the level of oil, coolant, brake fluid, windshield wiper fluid diagnostics of the general condition of the car: electricity, steering system, brake system, air conditioning system check of oil level in a transmission (to top up if necessary) oil change in the combustion engine diagnostics of a running gear greasing of a cardan shaft replacement of the oil filter replacement of the cabin filter replacement of the air filter replacement of the fuel filter wheel alignment

Type C maintenance – every 30 000 km: check the level of oil, coolant, brake fluid, windshield wiper fluid diagnostics of the general condition of the car: electricity, steering system, brake system, air conditioning system check of oil level in a transmission (to top up if necessary) oil change in the combustion engine diagnostics of a running gear replacement of the oil filter replacement of the cabin filter replacement of the air filter replacement of the fuel filter wheel alignment replacement of brake fluid

Type D maintenance – every 60 000 km: check the level of oil, coolant, brake fluid, windshield wiper fluid diagnostics of the general condition of the car: electricity, steering system, brake system, air conditioning system check of a drive belt of hinged units and a set of rollers oil change in the combustion engine diagnostics of a running gear greasing of a cardan shaft replacement of the cabin filter replacement of the oil filter replacement of the air filter replacement of the fuel filter wheel alignment replacement of radiator coolant replacement of brake fluid change of oil in a transmission

(II) Tire installation work:

Description

Basic tire work for one car for 4 wheels

(IІІ) Car body repair:

Description

The cost of a standard hour for the overhaul of the car body

(ІV) Engine repair, electrical equipment and main spare parts:

The main list of spare parts and works

Diagnosis, cleaning and antibacterial treatment of the air conditioning system

Checking electrical consumers and switches

Checking the condition of the battery

Vacuuming and refueling the air conditioning system

Intercooler purge

Cleaning the air conditioning system

Computer diagnostics

Wheel balancing

Express car wash

Complex car wash (interior, body)